## Slide 8
Population Density

## Slide 9
Population Density

## Slide 11
https://windexchange.energy.gov/maps-data/321

## Slide 22
San Gorgonio Pass, CA

## Slide 23
In Africa there is Some Wind Power
South Africa
Namibia
Somalia/Somaliland
And the Sahel
Have the greatest promise

## Slide 24
In Africa there is Some Wind Power

## Slide 25
https://www.cnbc.com/2017/09/08/a-wind-farm-of-epic-proportions-is-taking-shape-in-africa.html
Kenya Wind Farm 300 MW
Lake Turkana

## Slide 26
Betz Limit: 59.3% efficiency
A) Consider an ideal wind turbine that extracts 100% of the fluid energy, vout = 0.
Power output is 0.
vout
vin
B) For an ideal wind turbine that extracts 0% of the fluid energy, vout = vin.
Power output is 0.
Efficiency, Cp
vout/vin
Power is proportional to vin3
Under optimum condition vout/vin = 1/3
16/27 or 59.3% of energy is extracted
S is area of turbine
r density of fluid

## Slide 27
Betz Limit: 59.3% efficiency
vout
vin
Force
F = ma
= m dv/dt
= dm/dt Dv
= rSv (vin –vout)
Energy
dE = F dx
Power
P = dE/dt
= F dx/dt
= F v
P = rSv2 (vin –vout)
Kinetic Energy
E = ½ mv2
P = dE/dt = ½ (dm/dt) v2
P = dE/dt = ½ (dm/dt) v2in - ½ (dm/dt) v2out
= ½ (dm/dt) (v2in - v2out)
Continuity
(dm/dt) = rSv
Power
P = ½ rSv (v2in - v2out)
Power
½ rSv (v2in - v2out) = rSv2 (vin –vout)
½ (v2in - v2out) = ½ (vin - vout) (vin + vout) = v (vin –vout)
v = ½ (vin + vout)

## Slide 28
Betz Limit: 59.3% efficiency
vout
vin
v = ½ (vin + vout)
Power
P = ½ rSv (v2in - v2out)
= ¼ rS (vin + vout) (v2in - v2out)
= ¼ rS v3in (1 – (vout/vin)2 + (vout/vin) - (vout/vin)3)
Find Maximum Power at dP/d(vout/vin) = 0
(vout/vin) = 1/3
Plug into Power
Max Power = (16/27) (1/2) rS v3in
Incident Power = (1/2) rS v3in
-Power increases rapidly with wind speed
(this limits the wind range in which
a turbine can safely operate)
- (Max Power)/(Incident Power) = 16/27 = 0.593

## Slide 30
http://www.rebelwolf.com/essn/ESSN-Aug2005.pdf
A small wind turbine can expect Cp = 35%

## Slide 31
Two main types of wind turbine:
Drag (like a water wheel)
Lift (modern wind turbine)
The axis of rotation for the wind turbine can be horizontal or vertical.

## Slide 32
Wheel can’t move faster than the wind
½ of the area is wasted

## Slide 33
Drag based horizontal wind turbine
Slow speed is good for grinding grain (not good for electrical power generation)
Mechanical furling

## Slide 34
Middletown RI

## Slide 35
Drag based horizontal wind turbine
Slow speed is good for pumping water (not good for electrical power generation)
Tail allows furling of the turbine

## Slide 38
Up wind or down wind designs
Horizontal Axis Wind Turbine (HWAT)

## Slide 41
Vertical Axis Wind Turbine (VWAT)

## Slide 43
tsr
Ratio between the speed of the tip of the turbine blades and the wind speed

## Slide 44
More blades = more torque but lower RPM
For power generation 2 or 3 blades are optimum
For moving air or pumping water/grinding grain 5 blades or more.

## Slide 45
Massive power increase with wind speed
Alternator can’t handle this dynamic range
Design a turbine for optimum performance between 7 and 30 mph
Design to survive higher winds while still producing peak power
Options are:
Variable Pitch Blade: Tilt the blade (previous picture)
Tilt the entire turbine (old American west turbines)

## Slide 46
http://www.power-talk.net/blade-pitch.html

## Slide 47
http://www.power-talk.net/blade-pitch.html

## Slide 48
http://www.power-talk.net/blade-pitch.html

## Slide 53
Power Coefficient
Electrical Power/Wind Power

## Slide 55
Construction of a Large Wind Turbine on Land
This is generally done by power companies like Duke
So Chemical Engineers often become involved in managing
These large scale power production projects

## Slide 56
Components of A Wind Farm

## Slide 57
Components of A Wind Farm
Nacelle: the box located on the top of the tower, made of fiberglass, that contains approximately 8,000 subcomponents and connects them to the rotor. The size and weight of the nacelle vary depending on capacity (75 tonnes for a 2 megawatt (MW) turbine).
•Rotor and blades: the rotor is typically composed of three rotor blades, the rotor
hub that holds the blades in position as they turn and a pitch mechanism that allows the blade to rotate in the direction of the wind, maximising its capacity to harness wind.
• Tower: the nacelle is mounted on the top of a high tower that allows using the best winds and avoiding obstacles. Towers for large wind turbines may be either tubular steel towers, concrete towers, or lattice towers.
In addition to the wind turbine, other components are needed to install and operate a wind farm, such as the following: •Transformers to increase the voltage of the
electricity generated. The system inverters generate power output at approximately 480 volts. Electricity grids operate usually in kilovolts.
Capacitors to adjust the power factor and reduce the reactive energy generated.
The electric installation requires cables to connect wind turbines to the inverters, transformers and grid. The installation includes
contactors, circuit breakers and bypass contactors.
• Control equipment compromising microprocessor control, feeding source, heat resistors and coils.
• Electric protection equipment with relays and contactors of auxiliary or protection elements.
• Metering equipment to measure and control the quantity of electricity produced and supplied to the grid, and the reactive power.

## Slide 75
https://www.youtube.com/watch?v=SBbBh5xZ1gQ
High Speed Construction of a Wind Turbine Site

## Slide 76
https://www.youtube.com/watch?v=MHS10eGjNq8
100 Seconds

## Slide 79
https://www.youtube.com/watch?v=XVj_YyvgMbE
Hand Layout of Turbine Blades

## Slide 81
https://www.youtube.com/watch?v=iY0oBGo0-W4
Large Scale Layout

## Slide 87
Offshore Wind Power

## Slide 88
Offshore Wind Power

## Slide 89
Offshore Wind Power

## Slide 90
Offshore Wind Power

## Slide 91
Offshore Wind Power

## Slide 92
Offshore Wind Power

## Slide 93
Offshore Wind Power

## Slide 94
Offshore Wind Power

## Slide 95
Offshore Wind Power

## Slide 96
Offshore Wind Power

## Slide 97
Scotland
Offshore Wind Power

## Slide 98
Offshore Wind Power
Construction of the first floating wind farm

## Slide 99
Offshore Wind Power
Wind Turbine Engineer

## Slide 100
http://www.instructables.com/id/DIY-1000-watt-wind-turbine/
Can/should you build a wind turbine?

## Slide 105
https://www.youtube.com/watch?v=o9EEHFKEckM

## Slide 106
https://www.wikihow.com/Build-a-Wind-Turbine

## Slide 108
http://mwands.com/store/wind-turbine-products/wind-turbine-generators?gclid=Cj0KCQiAi7XQBRDnARIsANeLIeuJ_ySg8h_VuxrAzPEIWaOvsSAJ4ktBl8IgBN_TRTITq8Oi3CnV6sYaAmWeEALw_wcB

## Slide 109
Intrepid Malawi youth William Kamkwamba

## Slide 110
https://www.google.com/url?sa=t&rct=j&q=&esrc=s&source=video&cd=&ved=2ahUKEwjk1OzO99H6AhUfj2oFHVPRA0UQtwJ6BAgIEAI&url=https%3A%2F%2Fwww.youtube.com%2Fwatch%3Fv%3DnNp21zTeCDc&usg=AOvVaw1JDf2eN3SEBBaySfFd7NVV
Future of Solid-State Wind Power Generation